## Slide 1: 2013 Product Roadmap

## Slide 2: 2013.Q2/Q3
Existing product line
 | Product | Changes
2013.Q2 | SVR-500 Pi-Vu Central Basic | Multi-stream support with dynamic display Camera Setup Wizard Camera AutoSetup
2013.Q3 | SVR-632 SVR-632U | Upgraded CPU & memory

## Slide 3
2013.Q3 SVR-800 series
SVR-800
NVR
Full HD
Monitor
Hub
    Multi-stream with dynamic display
    DSP platform
USB2.0 for external device
  Mouse, keyboard, Joystick
Network: RJ 45 (Giga LAN)
IO: 8DI/4 DO
Video: VGA/HDMI
Audio: MIC-in, line-in and line-out
2-4 bays (Hardware RAID),4TB/bay
E-SATA: Max. 8TB
•Local Video Display
-Compression MJPEG/MPEG-4 Part 2/H.264 baseline,
main, high profile
-Resolution 5Mp/3Mp/ Full HD/MegaPixel/FD1/CIF/QCIF
-Max. decoder Frame Rate D1:480fps, 720p:360fps, 1080p:150fps
-Split window 1x1,2x2,3x3,4x4(SVR-816)
-Max. resolution limitation: 5Mp x1
-Dual monitor (HDMI+VGA)
    -Live:20CH (Live 16CH+SEQ 4CH), Live 16CH+playback 4CH
    Redesigned unified UI
Recording performance
1080p x 16 or 96Mbps
Configuration: web, local
Live/playback: web, local
Camera Auto setup
Client software
-ipad/iphone/android
-256CH CMS software

## Slide 4
Model | Channel | HDD | RAID | Housing | DI/DO
SVR-808 | 8CH 5Mpx1+2Mpx7 | 2 | X | Desktop | X
SVR-816 | 16CH 5Mpx1+2Mpx15 | 2 | X | Desktop | X
SVR-816 plus | 16CH 5Mpx1+2Mpx15 | 2 | HW 0/1 | Desktop | X
SVR-816U | 16CH 5Mpx1+2Mpx15 | 4 + e-SATAx1 | HW 0/1/5/10 | 1U | O
2013.Q3 SVR-800 series

## Slide 5
Models | Local display performance
SVR-808 | 240fps@720p30 120fps@1080p30 80fps@3MP 50fps@5MP Support 1080p60
SVR-816 series | 480fps@D1 30 360fps@720p30 150fps@1080p30 50fps@5MP Support 1080p60
SVR-800 Series
Performance

## Slide 6
2013.Q4 SVD-832
control
Video stream
CMS software
Network camera
NVR
    DSP platform
    Redesigned unified UI
    32CH (management), Live:16CH, playback:4CH
    Support network camera and SEEnergy NVR
    Video wall mode (controlled by 1024CH CMS)
    Media player mode (Display NVR video)
    Multi-stream with dynamic display
USB2.0 for external device, Mouse, keyboard, Joystick
Network: RJ 45 (Giga LAN)
Video: VGA/HDMI
Audio: MIC-in, line-in and line-out
Video format :MJPEG/MPEG-4 Part 2/H.264 baseline, main, high profile
Resolution 5Mp/3Mp/ Full HD/MegaPixel/ FD1/CIF/QCIF
Max. decoder Frame Rate D1:480fps, 720p:360fps, 1080p:150fps
Split window 1x1,2x2,3x3,4x4
Max. resolution limitation: 5Mp x1
SVD-832

## Slide 7
2013.Q4 SVD-832
CMS
Manage NVR & Video decoder
Network camera
Network camera
NVR
Audio/Video stream
Audio/Video stream
Control
    Controlled by 1024CH CMS software
    Display live video stream from NVR & camera
SVD-832
SVD-832
SVD-832
SVD-832

## Slide 8
2013.Q4 SVD-832
Audio/Video stream
NVR
Network camera
Media player Mode
    Control NVR remotely
    Display live & playback
    Operated by mouse, keyboard, remote controller and joystick
SVD-832

## Slide 9
2013.Q4 Pi-Vu Central 2.0
Hub
Network camera
PC
Hub
NVR
CMS software Pi-Vu Central 2.0
    Central control NVR & SVD
    Max.1024CH
    Support Google Map
SVD-832

## Slide 10
2013.Q4 SVR-632S
Recording performance
  32CH,1280x1024, 2Mbps
8 bays: 2U housing
  4TB x 8
Video output: VGA
Audio IO: Microphone, line in & line out
USB x4
E-SATA x 1 (Max. 8TB)
RAID 0/1/5/10
8DI/4DO

## Slide 11
Multi-Stream
SVR-800
NVR
Hub
Remote access
Live view
320x240
Network camera
Smart Phone
Live video (JPEG)
Internet Explorer
Live, Playback (video streaming)
Router
Internet
iPhone/iPad client software
Live, Playback (video streaming)
1920x1080
320x240
Recording
1920x1080
Live view
640x480
640x480
Strream1
Stream 3
Stream 4
1920x1080
640x480
320x240
Live/Rec
Live/Rec
Remote
Resolution
Function
Camera setup
Stream 2
1280x720
Live/Rec

## Slide 12
Dynamic Display
640x480
1280x1024
1920x1080
640x480
1280x1024
1920x1080
Display real-time video on split screen
Network camera
Get video steam with different resolution from network camera
SVR-800
NVR
* Works with compatible multi-stream cameras only

## Slide 13
2012-2013 Product Roadmap
Channel /video performance
SVR-204
2 bay
SVR-500
2 bay
SVR-632U
4 bay
SVR-632S
8 bay
2012.Q1
2013.Q1
SVR-808
SVR-816
SVR-816+
2 bay
SVR-816U
4 bay
SVD-832
Low
End
Middle
End
High
End
Display performance
Display performance
Channel/storage performance

## Slide 14
Product Profile
Enterprise
Small office
NVR server
NVR with local display
CMS Software-Pi-Vu central
Video Decoder SVD-832
SVR-632
SVR-632U
SVR-632S
SVR-504
SVR-508
SVR-516
SVR-516+
SVR-204
Entry
level
SVR-808
SVR-816
SVR-816+
SVR-816U